## Slide 1: Regulatory Update Briefing for the NYECC Board of Directors In-Person Meeting
September 13, 2023
Presented by George Diamantopoulos, Esq.

## Slide 2: 22-E-0064 - Con Ed Petition for Authorization and Cost Recovery for the Reliable Clean City – Idlewild Project – Estimated Capital Cost of $1.2B
Petition filed 8/22/23 asking the PSC to act by its 11/16/23 session.
By 2026, load growth will exceed peak design capability of the Jamaica Distribution Area Substation so Con Ed proposing to split the network into a smaller Jamaica network and the new Springfield network ($242M for feeders etc.), build the new Eastern Queens Transmission Substation (approx. $592M) and Idlewild Distribution Area Substation (approx. $380M) to supply the Springfield Network, and transfer 170 MW of load from the Jamaica Network Distribution Area Substation to the Idlewild Distribution Area Substation.
Project is not in the current electric rate plan because the Company proposed it too late in the rate case for review by DPS Staff.
$1.2B recovery either by surcharge if in service before next rate plan or through base rates in subsequent rate filing. May 2028 completion date so no rate impact under the current plan ending 12/31/25.
Discovery requests from DPS and responses from Con Ed are ongoing.

## Slide 3: Joint Proposal (JP) in Con Edison Steam Rate Case (22-S-0659)
NYECC is not a signatory to the Joint Proposal
3 year Rate Plan from 11/1/23 – 10/31/26 (RY1-RY3 - 11/1/23-10/31/24, 11/1/24-10/31/25, 11/1/25-10/31/26
Levelized increase is $77.8M per year. The cumulative 3 year levelized increase in the revenue requirement is $466.8M, which is $100M less than Con Edison’s initial ask.
  Levelized percentage Increases:
RY1 - (14.6% customer bill impact);
RY2 - (12.8% customer bill impact);
RY3 - (11.3% customer bill impact).
43.9% in Total Bill increases through end of RY3

## Slide 4: Customer Charges in JP (22-S-0659)
Steam Service Class | Current (2022) | RY 1 | RY 2 | RY 3
SC 1 | $1,259.52 | $1,526.43 | $1,802.43 | $2,089.43
SC 2 Rate I / SC4 Rate I | $4,147.03 | $4,923.43 | $5,573.43 | $5,573.43
SC 2 Rate II / SC4 Rate III | $6,754.91 | $7,527.43 | $7,527.43 | $7,527.43
SC 3 Rate I / SC4 Rate II | $3,010.96 | $3,555.43 | $4,098.43 | $4,558.43
SC 3 Rate II / SC4 Rate IV | $2,498.84 | $2,929.43 | $3,357.43 | $3,787.43

## Slide 5: Weather Normalization Adjustment (WNA) in JP (22-S-0659)
To mitigate the impacts of weather on the Company’s steam revenues and on steam customers’ bills, the Company will implement a WNA for the period of November through April of each year.
Structure based on current Gas WNA
Adjustments would be made to customer bills based on differences between actual and normal HDDs in each billing cycle.
Would apply to SCs 1, 2, 3, and 5, who use steam for space heating.
Does not apply to SC4 back up/supplementary which is intermittent usage.
Will be applied to total customer steam usage and will be applied as a per Mlb surcharge or surcredit.
By 6/30 each year, the Company will report on and file the prior winter’s monthly weather normalization adjustment revenue by customer class and in the aggregate.
If the Company implements the WNA outside of its new billing system, the Company will make a compliance filing with the Secretary that describes its alternative process for applying the weather normalization surcharge/surcredit on customers’ bills. The Company will provide to the parties its method of providing steam customers with the applicable information concerning the surcharge or surcredit amount and how it will be applied.

## Slide 6: Decarbonization Projects in JP (22-S-0659)
Steam Production Decarbonization Plan – Steam Decarbonization Plan withdrawn from this case (except maintains $3M for the Industrial Heat Pump), subject to Future Decarbonization Project Approval Mechanism.
Steam Distribution Decarbonization Plan (Hot Water Loop Decarbonization Project) – Reflect $0.5 million in this case to explore and conduct prep work.
Thermal Storage – Company will evaluate a thermal storage project through the Future Decarbonization Project Approval Mechanism that could replace 50,000 mmbtu/year of gas with electricity and result in a direct CO2 reduction of approximately 3,000 tons/year. The Company will schedule a meeting to discuss its feasibility analysis by 6/30/24.
Decarbonization Study & Implementation Plan – Conduct a Decarbonization Study like the study required by the Commissions’ CLCPA Implementation Order and file the Study with an Implementation Plan by 12/31/24. Company may spend up to $3M. Prior to filing, the Company will send a draft Implementation Plan to stakeholders and hold a meeting to receive feedback.

## Slide 7: Future Decarbonization Project Approval Mechanism, Local Law 97 Compliance Assistance, in JP (22-S-0659)
Future Decarbonization Project Approval Mechanism – Company may file Petition(s) for permission to implement a surcharge for costs incurred to implement PSC approved decarbonization projects (subject to a 0.5% cap on total bill impact). May defer up to $3M for preliminary work on projects until PSC decides on cost recovery.
LL97 Compliance Assistance
  Coefficient – Within 90 days of filing the Decarbonization Study & Implementation Plan, the Company will hold a stakeholder meeting to discuss plans to request that the applicable City agency adjust the LL97 coefficient for the steam system.
  Energy Audits – Between 11/1/23-10/31/26, upon request, provide steam customers with a detailed analysis of a building’s energy usage patterns to identify areas of energy waste or excess usage and suggest upgrades to improve energy efficiency and minimize operating costs; develop outreach and education plan to inform customers of the audit program. These reports will include information on any available known funding or incentives to steam customers for energy efficiency, including steam system consumption and efficiency, steam trap surveys, heat loss surveys, 24/7 monitoring of steam traps through wireless sensors, digital control of Pressure Reducing Valve stations on the customer side to reduce heat loss, heat recovery to lower steam consumption and cooling water consumption, upgrades and tune ups to steam turbine and absorption style chillers, including insulation for reduced chiller losses and early/extended life equipment replacements and enhancements.

## Slide 8: Steam Customer Development in JP (22-S-0659)
Steam Customer Development
Steam Business Development Plan to be filed by 12/31/24:
The Company will hold two meetings in 2024 to receive stakeholder input while the Plan is being developed, and within 90 days of filing the Plan, the Company will hold a meeting to discuss the recommendations in the Plan.
Company may spend up to $0.75M to develop the Steam Business Development Plan
Outreach and Education
  Will continue educational workshops and meetings with building owners and managers, etc. to increase knowledge of steam benefits;
  Enhance website on conversion to steam from gas/oil;
  Take into account Steam Business Development Plan recommendations;
  Maintain annual reporting
A Discounted Steam Promotion Rate for PSC consideration will be filed by 3/31/25 and will be informed by a steam marginal cost study filed by 12/31/24

## Slide 9: Con Edison Gas System Long Term Plan - 23-G-0147 – filed 5/31/23
8/21/23 – NYECC filed Comments on Con Ed Gas System Long Term Plan
None of the GSLTP’s proposed pathway bill impact rate increases are realistically sustainable and will inevitably result in unjust and unreasonable rates for customers.
Analyses need to incorporate the additional potential effects of programs such as the Cap-and-Invest program and other projected potential beneficial effects on bill impacts and not only reflect detrimental bill impact effects on customers.
The Company should provide calculated bill impacts for each service classification, or at the very least, the SC1, SC2, SC3 classes, and use projected volumes for each customer class rather than using a constant value for the volume of gas delivered to a representative customer in order to derive “significant value in conducting a share of wallet analysis to understand the bill impact of each Pathway on customers’ affordability.
9/5/23 – Con Ed filed Reply Comments
9/12/23 – DPS Conference to discuss comments and reply comments